## Slide 1: Final Talk: An EMG-based Method For Finger Gesture Recognition 10.04.2018
Advisors: Marko Jovanovic, Stephan Jonas Department of Medical Informatics, Uniklinik RWTH Aachen

## Slide 2: Outline
Motivation
State of the art
Data
Pipeline
Results
Discussion
Conclusion

## Slide 3: Motivation
MediWeCo: Contribution to learning and teaching physiotherapy through feedback.
Classify finger movements from EMGs.
Control virtual objects with finger movements.
Interpretation of sign language.
Notes: - Contribute to MediWeCo project in order to refine the detection of the little finger movements in order to give constructive feedback to teaching and learning of physiotherapeutic skills.
- Classify finger movements from EMGs acquired with Myo with a neural network.
- Practical not only for sign language communication but also for military communication where sound based communication is not appropriate.

## Slide 4: Why electromyography?
Notes: With Electromyography we can measure the electrical activity of the muscles:
There are two kinds of EMG electrodes:
Surface EMG electrodes where is placed on the skin with adhesive, over the muscle of interest.
+Relatively cheap, noninvasive, and have a large pickup area
-Lot of crosstalk
Intramuscular EMG sensors
+Record focally from deep muscles +reduction of crosstalk
-Painful for patients and far from everyday applications

## Slide 5: Thalmic Myo
Why Myo?
  Safe, easy, cheap, non-invasive
  No gel to facilitate conductivity
  Wireless
Technical Characteristics
  3-axis gyroscope
  3-axis accelerometer
  3-axis magnetometer
  8 EMG sensors
Notes: Myo has: 8 EMG electrodes and in each cubbie there is a small circuit board, and there are two batteries tucked in different cubbies. The Myo is composed of 8 EMG surface dry sensors. These sensors measure the electrical activity of the muscles of the forearm at a sampling rate of 200 Hz with 8 bits of resolution for each sensor. The forearm muscles are responsible for the movements of the different parts of the hand. The Myo transmits its measurements to the computer via Bluetooth. Additionally, the Myo contains an inertial measurement unit (IMU) with 9 degrees of freedom (accelerometer, gyroscope, and orientation in the x, y, and z axes). Finally, the Myo comes with a proprietary system for recognizing 5 gestures of the hand: pinch, fist, open, wave in, and wave out.

## Slide 6: Goal: finger gesture recognition with Myo
Signals acquired with Myo
Work solely with EMG signals
For different finger gestures find best detection accuracy
Notes: Determine the best combination of features -> best detection accuracy among the different finger gestures.
Due to the fact that for the experiments finger gestures will be examined, (NO ARM MOTION) the arm of the subject will not be moved, will remain still, so no IMU data will be needed. So, I will focus only on acquiring EMG signals from Myo.

## Slide 7: Outline
Motivation
State of the art
Data
Pipeline
Results
Discussion
Conclusion

## Slide 8: State of the art
Robotic arm control
Control of stage effects
Surgery interface control
Sign lagnuage recognition
Notes: -There is a prosthetic arm attached directly to his skeleton, and uses two Myo armbands on his upper arm to detect the electrical activity of his muscles. When he thinks about moving his prosthetic hand, he is able to do it. To start using his robotic arms Baugh had to undergo surgery at Johns Hopkins Hospital known as targeted muscle reinnervation. Revolutionizing Prosthetics Program, is almost at decade long project to create a neurally controlled artificial limbs to amputee patients is funded by the Defense Advanced Research Projects Agency (DARPA).
-A medical imaging firm from Spain called TedCas they used Myo armband, various cameras, and voice recognition software to give surgeons total control over the information they need during an operation: it’s a multi-sensor solution for operating rooms all connected to a device called the “TedCube”. So Myo can be used by surgeons in Spain to navigate through medical records while in the middle of surgery.
A group of students from the University of Texas at Dallas they achieved real-time American Sign Language Recognition using Wrist-worn Motion and Surface EMG sensors.
To do the recognition, we created an automatic adaptive segmentation technique to determine the period when a gesture is performed. 76 features from sEMG signal and 192 features from inertial sensors are studied and the best subset features are selected based on a feature ranking algorithm. Four different classification algorithms are evaluated, which are Decision Tree, Nearest Neighbor, Naïve Bayes and Support Vector Machine.
-Armin van Buuren controlled the stage effects during his performance such as control stage lights in real time with his hands

## Slide 9: Outline
Motivation
State of the art
Data
Pipeline
Results
Discussion
Conclusion

## Slide 10: Finger gestures
Extensions
Extensions
Flexions
Flexions
G1
G2
G3
G4
G5
G6
G7
N=21

## Slide 11: Finger gestures cont‘d
Extension
Flexion
G14
G8
G9
G10
G11
G12
G13
Extension
Flexion

## Slide 12: Outline
Motivation
State of the art
Data
Pipeline
Results
Discussion
Conclusion

## Slide 13: Pipeline overview
EMG acquisition with Myo
Artifacts removal
Individual movements segmentation
Data division into 11 folds
Windowing
Feature extraction
Classification
Detection accuracies
+Video
Notes: Here we see the different steps to preprocess the data through different methods and import them in the classifier for classification.

## Slide 14: Data collection

## Slide 15: Data division

## Slide 16: Windowing

## Slide 17: Feature extraction

## Slide 18: Train & classification

## Slide 19: Multilayer Perceptron
Notes: “Sequential” learning means that a given input pattern is forward propagated, the error is determined and back-propagated, and the weights are updated.
Then the same procedure is repeated for the next pattern.

## Slide 20: Outline
Motivation
State of the art
Data
Pipeline
Results
Discussion
Conclusion

## Slide 21: Results
Notes: Results from NN with HL=1 and HN=5
  with step 1, step 64 and one feature per training
We started using a dataset which consisted of extensions and flexions of my thumb. We used a neural network with 1 hidden layer and 5 hidden neurons. During the windowing, the stage before the feature extraction we used a step of one. And we got these detection accuracies. Because of the big load of data the runtime was very considerably long. So we decided to increase the step of windowing from 1 to 64. So we saw that the detection accuracies increased while the runtime was decreased.

## Slide 22: Results
Notes: The average detection accuracies of 5NNs
  with two features per training

## Slide 23: Results
Notes:   with three features per training

## Slide 24: Results

## Slide 25: Evaluation data
Gesture | db8 | bior2.2 | coif3
G9 | 73.5 | 73.5 | 74.3

## Slide 26: Outline
Motivation
State of the art
Data
Pipeline
Results
Discussion
Conclusion

## Slide 27: Discussion
Fluctuation of detection accuracies for different number of layers.
Data quality.

## Slide 28: Outline
Motivation
State of the art
Data
Pipeline
Results
Discussion
Conclusion

## Slide 29: Conclusions & Further work
Extract more features.
Rectification and normalization of the data in order to apply methods to reduce the final size of the input vector.
Test with different neural network architectures such as convolutional, recurrent neural networks.