## Slide 1: Proposal Talk 02.10.2017
Ioannis Agalliadis Institute of Medical Informatics, Uniklinik RWTH Aachen

## Slide 2: Motivation
MediWeCo: Contribution to learning and teaching physiotherapy through feedback.
First to use combination of Myo & EMG signals.
Notes: -Contribute to MediWeCo project in order to refine the detection of the little finger movements in order to give constructive feedback to teaching and learning of physiotherapeutic skills.
-First to detect finger gestures with Myo and EMG signals.

## Slide 3: Gesture recognition?
Image analysis requires ...
Sensing gloves are expensive.
$$$
Motion capture requires ...
Notes: -good and steady lighting conditions and lots of space
-cost of the software, equipment and personnel required can potentially be prohibitive

## Slide 4: Why electromyography?
Measuring muscle activity
Thalmic Myo
  Safe, easy, cheap, non-invasive
  No gel to facilitate conductivity
  Wireless
Notes: There are two kinds of EMG: surface EMG and intramuscular EMG.
Myo has: 8 EMG electrodes and in each cubbie there is a small circuit board, and there are two batteries tucked in different cubbies.
On the front of the main board we found a Kinetis Cortex M4 120MHz processor, a NRF51822 bluetooth low energy tranceiver/processor under a can, and a vibration motor.
On the back there's a motion sensor.

## Slide 5: Goal: finger gesture recognition with Myo
Signals acquired with Myo.
Focus solely on EMG signals.
For different finger gestures find best detection accuracy.
Notes: Determine the best combination of features -> best detection accuracy among the different finger gestures.
Due to the fact that for the experiments finger gestures will be examined, the hand of the subject will not be moved, will remain still, so no IMU data will be needed. So, I will focus only on acquiring EMG signals from Myo.

## Slide 6: State of the art
Robotic arm control
Control of stage effects
Surgery interface control
Remote vehicle control
Notes: -There is a prosthetic arm attached directly to his skeleton, and uses two Myo armbands on his upper arm to detect the electrical activity of his muscles. When he thinks about moving his prosthetic hand, he is able to do it.
-Myo is being used by surgeons in Spain to navigate through medical records while in the middle of surgery
-Armin van Buuren controlled the stage effects during his performance such as control stage lights in real time with his hands
- Erth7 is a game where the user could remotely manoeuvre a vehicle with simple gesture recognition and explore the remote secret location thousands of miles away where the vehicle was situated.

## Slide 7: Methods
Extracted features:
  RMS
  STFT
  Moving average
  Wavelet transforms
Classifiers:
  kNN
  SVM
  ANN
Windowing
Segment the signal into individual movements
EMG signals and video (thumb flexion/extension) acquired with Myo
Removal of artifacts
Division of data into train, test and evaluation folds
Notes: I remove

## Slide 8: Methods
EMG & video acquired with Myo
Artifacts removal
Segment signal into individual movements
Divide data into 11 folds
Windowing
Feature extraction
Classification
Detection accuracies

## Slide 9: Tasks

## Slide 10: Tasks

## Slide 11: Tasks

## Slide 12: Tasks

## Slide 13: Tasks

## Slide 14: Timeline
2017
2018
Dec
Jan
Feb
Mar
Thesis Registration
12/2017
Project Hand-Off
03/2018
11/2017 – 12/2017
Combine most accurate Features -> Results
12/2017 - 01/2018
Test forward selection &
backward elimination, creation of new gesture database
03/2018 - 03/2018
Discussion & Conclusion
Acquire new EMG signals
01/2017 - 03/2018

## Slide 15: Summary
What I will do
  Test new finger gestures.
  Find the optimal parameters for the classifiers.
  Combine the best feature sets to increase the detection accuracies.
  Create new finger gesture database.